## Slide 1: Laser Lab(s)
Peter Mueller

## Slide 2: Laser Spectroscopy of Radioactive Isotopes
https://www.gsi.de/en/start/forschung/forschungsfelder/appa_pni_gesundheit/ atomphysik/research/methoden/laserspektroskopie/survey.htm
Nuclear charge radii + nuclear moments
New opportunities with CARIBU & ATLAS upgrade

## Slide 3: CARIBU Isotopic Menu for Laser Spectroscopy
Low-energy yield, s-1
> 106
105 - 106
104 - 105
103 - 104
102 - 103
10 - 102
1 - 10
< 1

## Slide 4: Laser Spectroscopic Techniques
Collinear spectroscopy
In-trap spectroscopy
Ion Trap
Ion Source
90o Deflector
Laser Beam
High spectroscopic resolution
High sensitivity through bunched beams
Measure for the first time: Pd, Sb, Rh, Ru
Extend isotopic chains: Y, Zr, Nb, Mo
Ion beam line elements designed (with Mainz University & TU Darmstadt)
Offline tests in 2014, Installation in 2015
High sensitivity: few to single ion
Open geometry, LN2 cooled linear Paul trap
Buffer gas cooling
Ion source and deflector constructed
Ion trap designed
Off-line tests with Ba+ 2015/16

## Slide 5: Laser Lab Layout @ CARIBU
AC
HEPA
Laser Enclosure
(~ 6’ x 10’)
Laser Table
(~ 3’ x 7’)
Ion Trap(s)
Collinear Beamline
Tape Station
Cf-252 source
80 mCi -> 1Ci
High-resolution
mass separator
dm/m > 1/20000
Gas catcher
RF Cooler & Buncher

## Slide 6: Laser Spectroscopy Layout at CARIBU
Collinear beam-line
Ion trap
CARIBU low-energy beam area
Limited area for low-energy experiments @ CARIBU
Installation only possible after Penning trap moved out end of 2014
Shared laser infrastructure for both experimental techniques

## Slide 7: Collinear Setup for CARIBU
7
Low-energy (10 – 30 keV) ion beam line
  Compact modular setup with charge exchange and fluorescence detection
  Developed at Mainz University & TU Darmstadt
  Operated at TRIGA Reactor at Mainz University
Compact, solid state laser system (DPSS + Ti:Sa + Frequency Doubler(s))
Deflector
Charge Exchange
Fluorescence
Detection
Ion Source
In collaboration with W. Nörtershäuser (TU Darmstadt) & Ch. Geppert (U Mainz)

## Slide 8: Collinear Setup for Light Isotopes (8B, 14..17C, ...)
8
Couple to in flight production + gas catcher + ECR type ion source
Study charge radii of light isotopes
High spectroscopic resolution through pump/probe technique

## Slide 9: Nuclear Spin Polarization in Solid Noble-Gas Matrix
Capture atoms in solid noble-gas matrix (Ne … Xe)
Optical pumping in situ
Spin precession detection with SQUIDs (stable isotopes) or decay asymmetry (radioactive isotopes)
Started feasibility studies for
  Optical pumping / nuclear polarization (initial tests with Yb)
  Measurements of nuclear magnetic moments (other rare earth, …)
Substrate
LHe
Noble gas ice
Optical pumping
Atomic beam
B
LDRD funding
Zheng-Tian Lu
Chen-Yu Xu
Jaideep Singh

## Slide 10: Some concluding thoughts
New opportunities with ATLAS Upgrade (AGFA, A=126, AIRIS)
  High intensity beams for in-flight production of light isotopes
  Atomic spectroscopy of Nobelium and beyond with AGFA
Limitations on CARIBU isotopic yields for laser spectroscopy
  Molecular fraction, Charge state distribution (2+/1+)
  Charge exchange in cooler/buncher or in-beam
  Population of metastable atomic states
Limitations in number of elements that can be done
  Not “universal technique”; each element different
Tight space limitations in CARIBU LE-beam area
  Need to wait until CPT moves out
  Benefits largely from extension of LE beams into tandem hall
Combination with decay spectroscopy ?
  Laser excitation provides high selectivity, i.e., isobaric & isomeric
  Resonance ionization to produce pure beams
  Laser polarization (in-matrix or in-beam)

## Slide 11: CARIBU Laser Laboratory
Ion optics elements assembly started
Off-line tests with Ba+ starting in 2015
High sensitivity: few to single ion
Open geometry, LN2 cooled linear Paul trap
Buffer gas cooling
Ion Trap
Ion Source
90o Deflector
Laser Beam
90 deflector Ion source
High spectroscopic resolution
High sensitivity through bunched beams
Measure for the first time: Pd, Sb, Rh, Ru
Extend isotopic chains: Y, Zr, Nb, Mo
Ion beam line elements under construction (with Mainz University & TU Darmstadt)
Offline tests in 2014, Installation in 2015
Technical design of charge exchange cell (Mainz Univ.)

## Slide 12: In-trap spectroscopy
open geometry, LN2 cooled linear Paul trap - buffer gas cooling - large light collection efficiency - few to single ion detection sensitivity
Linear Paul Trap
Ion Trap
Ion Source
90o Deflector
Laser Beam
Matt Sternberg
Alexandra Carlson
Luis Brennan

## Slide 13: Laser Spectroscopic Techniques
Collinear spectroscopy
In-trap spectroscopy
Ion Trap
Ion Source
90o Deflector
Laser Beam
High spectroscopic resolution
High sensitivity through bunched beams
Extend isotopic chains: Y, Zr, Nb, Mo
Measure for the first time: Rh, Ru
Design and construction in FY 2014
Installation @ CARIBU in FY 2015
High sensitivity: few to single ion
Open geometry, LN2 cooled linear Paul trap
Buffer gas cooling

## Slide 14: Laser Spectroscopy & Nuclear Structure
Nuclear ground state properties from atomic spectroscopy
Model independent, precision measurement
Atomic isotope shifts -> charge radii
Atomic hyperfine structure
-> nuclear spin and moments (single-particle & collective)

## Slide 15: Collinear Laser Spectroscopy
High spectroscopic resolution
High sensitivity through bunched beams
Neutral atoms w/charge-exchange
  Measure for the first time: Rh, Ru,
  Extend isotopic chains on: Mo, Nb, …

## Slide 16: The Boron-8 Collaboration
P. Bertone1, Ch. Geppert2, A. Krieger2,3, P. Mueller1, W. Nörtershäuser2
1 Physics Division, Argonne National Laboratory
2 Institut für Kernphysik, TU Darmstadt
3 Institut für Kernchemie, Universität Mainz
16

## Slide 17: The Proton Halo Nucleus 8B
Proton halo might not show
an extended matter radius
due to the coulomb barrier
17

## Slide 18: 8B in the FMD
Simple picture of 8B:
7Be core in 3/2- g. s. and a weakly bound proton in p3/2 orbital.
Intrinsic densities of the proton-halo candidate 8B calculated in the fermionic molecular dynamics model (courtesy of T. Neff – GSI).
18

## Slide 19: Laser Transitions in Boron Ionic Systems
1s 2 2s 2 1S0
2s 2p 1P1o
136 nm
B+: 4e-
Be-like
1s 2 2s 2S1/2
206.6 nm
206.8 nm
1s 2 2p 2P1/2
2s 2p 3PJ
0
1
2
2s 3s 3S1
324 nm
 12 eV
1s 2 2p 2P3/2
B2+: 3e-
Li-like

## Slide 20
Sn+ 5s 2S1/2 5p 2P3/2 : =215 nm
Two SHG*-steps: 860 nm  430 nm  215 nm
* SHG= Second Harmonic Generation
Short Detour ....

## Slide 21: Simple Structure in Complex Nuclei
1g
2d
3s
1h
1g9/2
1g7/2
2d5/2
2d3/2
3s1/2
1h11/2
1h9/2
50
58
64
68
70
82
92
50
82
Capacity of 1h11/2 niveau: 12 neutrons
→ 6 quad. moments
But: 10 quad. moments
Neutron pairs shared between the neighboring levels.
D. T. Yordanov et al., Phys. Rev. Lett. 110, 192501 (2013)

## Slide 22: Shell-Model Prediction
slope determined by Qsp
single neutron  oblate deformation (Q<0)
single neutron hole  prolate deformation (Q>0)
Extraction of Qsp:

## Slide 23: Laser Transitions in Boron Ionic Systems
2s 3S1 (~150ms)
2p 3P0,1,2
282 nm
1s 2 2s 2 1S0
2s 2p 1P1o
136 nm
B+: 4e-
Be-like
1s 2 2s 2S1/2
206.6 nm
206.8 nm
1s 2 2p 2P1/2
E  200 eV
  6 nm
2s 2p 3PJ
0
1
2
2s 3s 3S1
324 nm
 12 eV
1s 2 2p 2P3/2
1s 2 1S0
B+: 3e-
Li-like
B3+: 2e-
He-like

23

## Slide 24: The atomic system of 8B (I=2)
F
4
3
2
1
0
1s2p 3P2
1s2p 3P0
2
36.441 cm-1


16.379 cm-1
3
2
1
1s2p 3P1
1s2p 3PJ Fine- and Hyperfine Structure
1s 2p 3P2 1s 2s 3S1 @ 282.5 nm
Transition Rates ( 107 /s)
3
2
1
F
4
3
2
1
0
4.6
3.0
1.6
1.6
2.7
3.1
4.6
3.4
1.1
16634
72.4
-12404
-20748
-24928
-1570120
-1583500
-1591550
-1092480
MHz
rel. 3P2
Calculations by G.W.F. Drake and Z.-C. Yan
24

## Slide 25: 8B Production Tests
6Li beam ~50 MeV
~100 pnA
3He target cell
LN2 cooled
6Li(3He,n)8B
SC Solenoid, 0.6 T
MWPC
4He Gas Catcher
Si detector
Particle ID
in MWPC via time-of-flight and position
-> ~ 10 8B / ppA
behind gas catcher on Si-detector -> ~ 1 count/s/ppA
2014 ATLAS intensity upgrade ~ 1 pA 6Li
25

## Slide 26: Roadmap to 8B at ANL: Ion Production
Requirements for 8B???
Atomic theory 
Nuclear theory 
Ion production: In-flight method
Stop, low energy B+ -> source … gas catcher 
Charge breeding
… to B3+ or B4+
Populate metastable state
  … in source or charge-ex.
High-resolution laser spec … collinear laser spectroscopy
26

## Slide 27: Roadmap to 8B at ANL: Ion Production
Requirements for 8B???
Atomic theory 
Nuclear theory 
Ion production: In-flight method
Stop, low energy B+ -> source … gas catcher
Charge breeding
… to B3+ or B4+
Populate metastable state
  … in source or charge-ex.
High-resolution laser spec … collinear laser spectroscopy
27

## Slide 28: Roadmap to 8B at ANL: Ion Production
Requirements for 8B???
Atomic theory 
Nuclear theory 
Ion production: In-flight method
Stop, low energy B+ -> source … gas catcher
Charge breeding
… to B3+ or B4+
Populate metastable state
  … in source or charge-ex.
High-resolution laser spec … collinear laser spectroscopy
28

## Slide 29: Roadmap to 8B at ANL: Ion Production – Charge Breeding
Need to produce low-energy (~20-50 keV) beam of metastable 8B3+ beam
Capture 8B in gas stopper and extract (10%)
Inject low emittance 8B+ beam from gas catcher into ECR source (10%)
Charge breed to B+ in ECR and accelerate to ~50 keV
  3+ efficiency of ~10% and metastable fraction of ~10% have been reported in the literature for neighboring C and Be
-> ~1x103 metastable 8B3+ (comparable to 12Be measurement)
Alternatives:
Extract 8B+ in molecular form from gas catcher and break up in ECR
Extract 8B4+ from ECR and populate metastable state in charge exchange cell
Other Transitions ?
Questions
many ….
What are the efficiencies in each step?
29

## Slide 30: Roadmap to 8B at ANL: Ion Production – Charge Breeding
Requirements for 8B???
Atomic theory 
Nuclear theory 
Ion production: In-flight method 
Stop, low energy B+ -> source … gas catcher 
Charge breeding
… to B3+ or B4+ 
Populate metastable state
  … in source or charge-ex. 
High-resolution laser spec … collinear laser spectroscopy
30

## Slide 31: Roadmap to 8B at ANL: How to Increase Detection Efficiency ?
Collinear spectroscopy collinear/anticollinear (see beryllium)
Detection of XUV photon/ ion coincidence with extremely low background
Alternatively with bunched beam (ECR bunched extraction?)
Questions:
Energy spread from ECR?
Sensitivity of detection scheme?
HFS splittings and transition strength?
First steps:
Layout of collinear beamline
Simulating beamline (SimION)
Commissioning and testing of components at TUD/Mainz  Transport to ANL
Test with stable isotopes (-> improve absolute measurements for QED test)
31

## Slide 32: Low Mass Region
32

## Slide 33: Hyperfine Structure and Nuclear Moments
Magnetic dipole
Electric quadrupole

## Slide 34: In-Trap Spectroscopy at CARIBU
Linear Paul trap for spectroscopy
  Initially with neutron-rich Ba+
  Isotope shift + moments (HFS)
  Use RF cooler / buncher & transfer line
To investigate:
  optimized trap geometry and detection system
  Buffer gas cooling + quenching (with H2)
  Cooling of trap with LN2
Future:
  other CARIBU beams
    High mass: Pr, Nd, Eu, …
    Low mass: Y, Zr, Nb, Sr, …
  Yb+ -> No+ with ATLAS Upgrade
Ba Isotopes